## Slide 1
ME-446 | COMPLEX ENGINEERING PROBLEM
AI-Based Building Energy Consumption
Prediction and Analysis for HVAC and
Energy Efficiency Applications
NED University of Engineering and Technology | Department of Mechanical Engineering
Group: [Group No.] Students: [Name — Roll No.] Instructor: [Instructor Name]
Fall Semester 2026 | Submission: 4 November 2026
Core finding: accurate for buildings with history; not validated for unseen buildings.
Dataset approval pending | Tableau workbook pending | Full-data run pending
Notes: Introduce the team. State the one-sentence takeaway: the model is accurate for known buildings but not for new ones. Mention that the local results are subset results and that approval, the Tableau workbook, and full-data metrics are pending.

## Slide 2
MOTIVATION
The engineering problem is conditional accuracy
ME-446 CEP | Fall 2026
2
• Buildings and HVAC systems account for a major share of electricity use.
• A normal-demand model can support monitoring, demand planning, and anomaly screening.
• Target: hourly electricity meter reading (meter 0) from building, calendar, and weather data.
• The real question: accurate for which buildings, and under what conditions?
High aggregate R² can hide poor transfer to new buildings.
Why it matters
• Peak demand drives capacity and cost.
• HVAC scheduling and setback decisions need a baseline.
• False anomaly alarms erode trust.
• Predictions are not measured savings or efficiency.
Notes: Explain why a mechanical engineer cares: peak demand, HVAC scheduling, avoiding false alarms. Do not claim savings. The key tension is that a high aggregate score can hide failure on new buildings.

## Slide 3
DATA
Dataset and local scope
ME-446 CEP | Fall 2026
3
12.06 M
electricity rows
1,413
electricity buildings
120
buildings in local subset
1.03 M
local hourly rows
• ASHRAE Great Energy Predictor III, accessed 20 October 2026 via KaggleHub.
• Full train: 20,216,100 rows, 1,449 buildings, 16 sites, four meter types.
• Electricity only (meter 0); 4.40% zero readings retained.
• Chronological split: Jan–Sep train / Oct–Nov validation / Dec test.
• Units: dataset energy units (documented as kWh), not independently verified.
All local metrics are subset metrics — not full-dataset results.
Teacher approval pending. Dataset uniqueness is not claimed.
Split: 769,122 train | 174,537 validation | 87,308 test
Notes: Be explicit that all local results are subset results. The subset preserves all 16 sites and all 16 primary uses but not the full building mix. Approval and uniqueness are pending.

## Slide 4
METHOD
Preprocessing is traceable and leakage-safe
ME-446 CEP | Fall 2026
4
Data handling
• Raw CSVs retained unchanged; typed Parquet intermediates.
• Missing metadata retained: year_built 51.76%, floor_count 70.90%.
• Weather: past-only forward fill, 3-hour limit.
• Negative precipitation and invalid pressure treated as missing.
• Explicit missing flags for cloud, precipitation, pressure.
Model features (24)
• Identity: building_id, site_id, primary_use.
• Size and vintage: square_feet, floors, year_built, age.
• Calendar: hour, day, month, weekend, cyclical encodings.
• Weather: air/dew temperature, wind, cloud, precipitation, pressure.
• No target lags, no future fill, no test-driven selection.
Leakage controls: chronological split + pipeline-fitted preprocessing + past-only weather fill.
Notes: Emphasize that weather fill uses only the past, and the test month is never used to choose the model. Missing values are not replaced by invented building ages.

## Slide 5
INSIGHT 1
Demand is right-skewed and building-dominated
ME-446 CEP | Fall 2026
5
Local subset: 1,030,967 hourly electricity readings.
• Median 59.05 vs mean 188.78.
• 99th percentile 2,454; maximum 41,552.
• Floor-area log correlation 0.750.
• square_feet is the top permutation feature.
Benchmark within building/use groups; normalize by floor area.
Notes: The mean is not the typical building. A single global average is a poor benchmark. This motivates size- and use-normalized comparisons.

## Slide 6
INSIGHT 2
Occupancy schedules create a weekday and midday cycle
ME-446 CEP | Fall 2026
6
Local subset: hourly, daily, and monthly demand patterns.
• Weekday mean 195.44 vs weekend 172.24.
• Weekday/weekend ratio 1.135.
• Peak at 13:00; trough at 03:00.
• August highest monthly mean: 215.14.
Target setback and scheduling studies at low-occupancy hours.
Notes: The cycle is consistent with occupancy and cooling, but the data have no occupancy labels. Do not claim that a schedule change will save energy without measurement.

## Slide 7
INSIGHT 3
Temperature response is site-specific
ME-446 CEP | Fall 2026
7
Per-site temperature response; pooled correlation masks opposite regimes.
• Pooled r = −0.074 looks weak.
• Site r ranges −0.134 to +0.406.
• Site 11 rises from 265.74 to 377.17.
• Sites 6, 7, 10 are negative.
Use site interactions or degree hours, not one global coefficient.
Notes: This is a pooled-correlation trap. Opposite heating and cooling responses cancel. A single global temperature coefficient is inadequate.

## Slide 8
METHOD
Three regressors, one pre-declared selection rule
ME-446 CEP | Fall 2026
8
Linear Regression
Interpretable baseline
One-hot; median imputation; scaling; sparse design matrix
Random Forest
Nonlinear interactions
80 trees; depth 16; min leaf 20; 250,000-row sample
HistGradientBoosting
Efficient boosting
200 iterations; lr 0.08; 31 leaves; all 769,122 rows
Selection rule: lowest validation RMSE. Test evaluated once after selection.
Metrics: MAE, RMSE, R², RMSLE | Seed 42 | Identical held-out rows
Notes: Explain why RMSE: large peak errors are costly for demand planning. The mean baseline is a reference, not a candidate. All models use the same split.

## Slide 9
RESULTS
HGB wins validation RMSE; RF wins MAE and RMSLE
ME-446 CEP | Fall 2026
9
Model | Val RMSE | Test MAE | Test RMSE | Test R² | Test RMSLE
Mean baseline | 411.67 | 209.57 | 406.05 | −0.001 | 1.920
Linear Regression | 223.03 | 61.39 | 154.51 | 0.855 | 0.942
Random Forest | 166.92 | 32.05 | 78.90 | 0.962 | 0.448
HistGradientBoosting | 165.74 | 33.20 | 69.78 | 0.970 | 0.591
• HGB: best validation RMSE, test RMSE, and test R².
• Random Forest: slightly lower MAE and better RMSLE.
• HGB fit about 4.3× faster than RF (53.9 s vs 232.4 s).
• Trade-off is reported; RMSE prioritizes large peak errors.
Notes: Do not say HGB dominates every metric. The choice depends on whether peak RMSE or typical MAE is the operational priority. The selection rule was fixed before test evaluation.

## Slide 10
CRITICAL FINDING
The high R² does not transfer to unseen buildings
ME-446 CEP | Fall 2026
10
Group | MAE | RMSE | R² | RMSLE
Seen buildings, test | 33.86 | 74.15 | 0.971 | 0.595
Unseen buildings, test | 150.51 | 321.33 | −0.555 | 1.525
• 20% of buildings held out entirely, stratified by site.
• Unseen predicted mean 242.49 vs actual 176.99.
• building_id is a top-three feature.
• December: 126 zeros vs 44,796 in training.
This is building-specific interpolation, not a universal physical model.
HGB trained without the held-out buildings.
Notes: This is the most important slide. The main model relies on building identity. Do not deploy to new buildings without calibration or richer descriptors. The test month also has a different zero-reading distribution.

## Slide 11
DEMONSTRATION
Two held-out rows, two very different stories
ME-446 CEP | Fall 2026
11
Case | Building | Time | Actual | Predicted | Error
High demand | 1088 | 19 Dec 15:00 | 3,427.60 | 3,417.33 | 0.30%
Typical | 386 | 9 Dec 06:00 | 41.16 | 41.16036 | 0.0009%
• Building 1088: 287,594 ft² education building at −10.6 °C; high winter load is plausible.
• The near-exact typical case is not proof of generalization; trees can match a leaf closely.
• The feature-consistency check between training SQL and Python inference passed.
• The building-holdout experiment is the real generalization test.
These are unseen rows, but the buildings are still known to the main model.
Notes: Be precise: the rows are unseen, but the buildings are in the training data. The near-exact second case should not be oversold. The holdout experiment shows the real transfer performance.

## Slide 12
DELIVERABLES
Dashboard: data and guide complete, workbook pending
ME-446 CEP | Fall 2026
12
Energy Overview
Totals, averages, building/site counts, trend
Weather & Building
Temperature, schedules, use, size
Model Performance
Comparison, residuals, error groups
• Tableau-ready CSVs: 1,030,967 electricity rows; 349,232 prediction rows.
• Detailed dashboard specification and step-by-step Tableau build guide.
• Supplementary Streamlit app with four pages; smoke-tested with AppTest.
• Reproducible notebook, 22 passing tests, audit, report, and five insights.
No Tableau workbook has been authored, published, or tested.
Streamlit is supplementary; it does not replace Tableau.
Notes: Be explicit about the dashboard status. Data and instructions are complete; authoring and validation remain. Do not show a fabricated Tableau screenshot.

## Slide 13
ENGINEERING INTERPRETATION
Five insights translate into concrete actions
ME-446 CEP | Fall 2026
13
1
Demand is right-skewed and building-dominated
Benchmark within peer groups; normalize by size.
2
Weekday/midday cycle
Target setback and scheduling studies.
3
Temperature response is site-specific
Add degree hours or site interactions.
4
Primary use and site dominate
Segment models and dashboards.
5
Seen-building accuracy does not transfer
Calibrate before new-building use.
Add past-only history features, model zero/non-zero separately, calibrate residuals, validate on a future year.
Notes: Connect each insight to a concrete action. Avoid claiming causal savings. The fifth insight is the main deployment caution.

## Slide 14
CONCLUSION
Conclusion: a useful monitoring tool, not a universal predictor
ME-446 CEP | Fall 2026
14
• HGB test R² 0.970 on seen buildings; MAE 33.20, RMSE 69.78.
• Unseen-building R² −0.555; MAE 150.51 — a critical limitation.
• Results are 120-building subset results from one year.
• Winter-only test, zero-reading shift, site-level weather, missing metadata.
• Tableau workbook, full-data run, and teacher approval remain pending.
Next: full-data Colab run, history features, degree hours, two-stage zero model, Tableau workbook.
Do not use the model for a new building without calibration.
Questions?
Notes: End with the conditional conclusion. Invite questions about generalization and operational use. Keep the caveats visible.

## Slide 15
REFERENCES
References and project evidence
ME-446 CEP | Fall 2026
15
• ASHRAE. (2019). Great Energy Predictor III. Kaggle.
• Miller, C., et al. (2020). The ASHRAE Great Energy Predictor III competition: Overview and results. Science and Technology for the Built Environment, 26(10), 1427–1447.
• Amasyali, K., & El-Gohary, N. M. (2018). A review of data-driven building energy consumption prediction studies. Renewable and Sustainable Energy Reviews, 81, 1192–1205.
• scikit-learn, pandas, Tableau, and Streamlit documentation.
Evidence: README.md | reports/technical_report.md | reports/engineering_insights.md | reports/tables/ | reports/figures/
Thank you.
Notes: Thank the audience and invite questions. Keep this slide visible during Q&A.